## Slide 2: MODULE-2
VERILOG HDL CODING STYLE
Ports and Modules
Lexical Conventions
Data Types
Operators
Gate Level Modeling
Data Flow Modeling
Behavioral level Modeling
Test Bench
2

## Slide 3
3

## Slide 4: INTRODUCTION TO HDL
The sequential model used in traditional programming languages (i.e. “C”) cannot capture the characteristics of digital hardware, and there is a need for special languages (i.e., HDLs) that are designed to model digital hardware.
The fundamental characteristics of a digital system are defined by the concepts of entity, connectivity, concurrency and timing.
HDL is a language used to describe digital system.
The goal of an HDL is to describe and model digital systems faithfully and accurately.
4

## Slide 5: INTRODUCTION TO HDL
much like a
A hardware description language looks programming language such as C.
Different HDLs are available different purpose such as Analog system design , digital system design, PCB design.
The two main HDLs are Verilog and VHDL for digital system design.
There are other, limited capability, languages such as ABEL, CUPL, and PALASM that are tailored specifically for PALs and CPLDs.
5

## Slide 6: INTRODUCTION TO VERILOG HDL
VERILOG HDL – VERIfiable LOGic HDL: Programming language used to describe digital circuits and systems
It is most commonly used in the design and verification of digital circuits at the register-transfer level of abstraction.
It is also used in the verification of analog circuits and mixed-signal circuits.
One of the two most common HDL used by IC designers (another one is VHDL)
6

## Slide 7: INTRODUCTIONTO VERILOG HDL
Similar to C/Pascal programming language
Verilog Modeling ranges from Gate to Processor level and it provides flexibility for creating used defined primitives
In-build primitive logic gates (AND, OR, NAND etc) and switch-level primitive gates (nmos, pmos, cmos etc)
Verilog versions: Verilog-95, 2001, 2005, System Verilog 2009, 2012
Verilog is case-sensitive and its file extension is .v

## Slide 8: INTRODUCTIONTO VERILOG HDL
Verilog HDL Simulators
Commercial:
  Xilinx ISE
  Active HDL
  Model sim
  Quartus-II
  MP Sim
Open sources:
  Verilator,
  Icarus verilog,
  GPL cver,
  VeriWell
Online:
  iverilog.com,
  EDAPlaygro und.com,
Tarang EDA

## Slide 9: VERILOG vs VHDL

## Slide 10: STRUCTURE OF VERILOG HDL

## Slide 11: A SIMPLE VERILOG PROGRAM
Verilog Code
Circuit
// A simple example
module and2 (a, b ,c);
input a, b;
output c;
assign c = a & b;
endmodule
a
b
c
comment line
module name port list
port declarations
body
end module

## Slide 13: MODULE
Modules are the basic building blocks in Verilog. A module definition starts with the keyword module ends with the keyword endmodule
  Elements in a module
    Interface: consisting of port and
parameter declarations
    optional add-ons
    body: specification of internal
part of the module
module name (port_list)
port declarations parameter declarations
`include directives
variable declarations assignments low-level module instantiation initial and always blocks task and function
endmodule

## Slide 14: MODULE - EXAMPLE
General definition
module module_name ( port_list ); port declarations;
…
variable declaration;
…
description of behavior endmodule
Example
module HalfAdder (A, B, Sum Carry); input A, B;
output Sum, Carry; assign Sum = A ^ B;
//^ denotes XOR
assign Carry = A & B;
// & denotes AND endmodule

## Slide 15: PORTS
Port provides interface, through which module can communicate its environment
Port connecting rules: inputs, outputs, inouts, width
matching, unconnected ports
All ports in the <port_list> must be declared in module. Ports can be declared as,

## Slide 16: PORTS - EXAMPLE
Verilog Code
Circuit
module MAT (enable, data, all_zero, result, status);
[3:0]
input input output
output [2:0]
enable; data; all_zero; result; status
// scalar input
// vector input
// scalar output
// vector output
// bi-directional port
Inout [1:0]
……
MAT
enable
data[3:0]
all_zero result[2:0] status[1:0]
LSB MSB
endmodule
To make code easy to read, use self-explanatory port names
For the purpose of conciseness, use short port names
In vector port declaration, MSB can be smaller index.
e.g. output [0:3] result (result[0] is the MSB)

## Slide 18: LEXICAL CONVENTIONS
Very similar to C
  Verilog is case-sensitive
  All keywords are in lowercase
  A Verilog program is a string of tokens
    Identifiers
    Escape Identifiers
    Keywords
    Comments
    Value Set
    Numbers
    Whitespace
    Strings

## Slide 19: LEXICAL CONVENTIONS
IDENTIFIERS
Identifiers are name given to objects
so that they can be
referenced in the design
Formed from {[A-Z], [a-z], [0-9], _, $}, but ..
.. can’t begin with $ or [0-9]
valid valid invalid invalid valid
myidentifier
m_y_identifier
3my_identifier
$my_identifier
_myidentifier$
Case sensitivity
myid  Myid

## Slide 20: LEXICAL CONVENTIONS
ESCAPE IDENTIFIERS
It provides the way of including any of the printable ASCII characteristics in an identifiers
It begin with back slash (\) and end with white space
Some of examples are
  \a*b*c
  \**print value**
  \4000
An escaped keyword is not treated as same as the keyword
The identifier \ begin is distinct from the identifier begin
  myname  \myname

## Slide 21: LEXICAL CONVENTIONS
KEYWORDS
Keywords are predefined, special identifiers that define the language constructs
All key words defined in lower case
Some of them are
  input, output, inout
  reg, wire, task, tri, time,
  pmos, nmos, and, or, not, wor, xnor,
  begin, parameter, buf, edge, join, medium,wait, use
  if,else, case,while, always, initial, posedge, negedge, assign
  end, endtask, endcase, endfunction, default, endtable, endmodule

## Slide 22: LEXICAL CONVENTIONS
COMMENTS
//The rest of the line is a comment
A= x^y; // this is single line comment
/* Multiple line comment*/
/* this is example of multiline comment A= x^y;
C=a+b; */
/* Nesting /* comments */ do NOT work */

## Slide 23: LEXICAL CONVENTIONS
VALUE SET
represents low logic level or false condition represents high logic level or true condition
represents unknown logic level represents high impedance logic level

## Slide 24: LEXICAL CONVENTIONS
NUMBERS
Number Specification
  Sized numbers
  Unsized numbers
  Unknown and high-impedance values
  Negative numbers
Underscore character and question marks
  Use ‘_’ to improve readability
    12’b1111_0000_1010
    Not allowed as the first character
  ‘?’ is the same as ‘z’ (only regarding numbers)
    4’b10?? // the same as 4’b10zz

## Slide 25: LEXICAL CONVENTIONS
NUMBERS
Sized numbers
  General syntax: <size>’<base><number>
    <size> number of bits (in decimal), not the number of hex or decimal digits
    <number> is the number in radix <base>
    <base> :
      d or D for decimal (radix 10)
      b or B for binary (radix 2)
      o or O for octal (radix 8)
      h or H for hexadecimal (radix 16)
    Examples:
– 4’b1111, 12’habc, 8’d255

## Slide 26: LEXICAL CONVENTIONS
NUMBERS
Unsized numbers
  Default base is decimal
  Default size is at least 32 (depends on Verilog compiler)
  Examples
    23232
    ’habc
    ’o234
Negative numbers
  Put the sign before the <size>
  Examples:
    -6’d35
    4’d-12 // illegal

## Slide 27: LEXICAL CONVENTIONS
NUMBERS
X or Z values
Unknown value: lowercase x or Uppercase X
  4 bits in hex, 3 bits in octal, 1 bit in binary
High-impedance value: lowercase z or Uppercase Z
  4 bits in hex, 3 bits in octal, 1 bit in binary
Examples
  12’h13x
  4’hX
  32’bz
Extending the most-significant part
MS bit = 0, x or z  extend this
– 4’b x1 = 4’b xx_x1
MS bit = 1  zero extension
– 4’b 1x = 4’b 00_1x

## Slide 28: LEXICAL CONVENTIONS
WHITE SPACE & STRINGS
Whitespace
  Blank space (\b)
  Tab (\t)
  Newline (\n)
Strings
  As in C, use double-quotes
  Examples:
    “Hello world!”
    “a / b”
    “text\tcolumn1\bcolumn2\n”

## Slide 30: DATA TYPES
NET
Two groups of data types:
  Net: it represents connection between hardware elements
  Registers: represents an abstract data storage element
Syntax for net declaration:
<net list> one of the net type
[msb:lsb] specify ranges of the net
Net is a value determined from the value of its drivers
Nets are one-bit value unless they are declared as vectors and default value of net is Z
Examples: wire a; wire b, c; wire d=1’b0;
<net_list> [msb:lsb] net 1, net 2,……….net n;

## Slide 31: DATA TYPES
Memory
Processor
r_w
data
addr
wire | [7:0] | data; | // vector signal
wire | [9:0] | addr; | // vector signal
…… |  |  | 
A net declaration starts with keyword wire
……
wire r_w; // scalar signal
Different kinds of net data types are:
Wire & tri-nets
Wor & trior nets
Wand & triand nets
Tri0 & tri1 nets
Supply0 & supply1 nets
(F)
Trireg nets
NET TYPES

## Slide 32: DATA TYPES
Memory
Processor
r_w
data[7:0]
addr[9:0]
clk
rst
status[3:0]
i_o[7:0]
module pc (clk, rst, status, i_o);
input clk, rst;
output [3:0] status;
inout [7:0] i_o;
endmodule
wire | r_w; | 
wire | [7:0] | data;
wire | [9:0] | addr;
…… |  | 
NET vs PORTS
Nets are internal signals that cannot be accessed by outside
Ports are external signals to interface with outside environment
  input ports can be written but cannot be read
  output ports can be read but cannot be written
  inout ports can be read and written

## Slide 33: DATA TYPES
REGISTERS
A register type represents data storage elements or a variable that can
hold a value
Do not represent real hardware but real hardware can be implemented with registers
It can assign a value only within always or initial statement and default
value of register is X
Example of how register can be used:
#5 CLK = ~CLK;
C = 0; // C is now 0
BECE102L – DIGITAL SYSTEM DESIGN
reg CLK; initial begin
CLK = 1'b0;
reg A, C; // declaration
always
A = 1;
C = A; // C gets the value 1 A = 0; // C is still 1

## Slide 34: DATA TYPES
REGISTERS TYPES
(a) INTEGER
A integer register contains integer variable
It is a general purpose register data type used for manipulating quantities, typically for high-level behavior
Value of MSB and LSB specify the range of an integer array
Examples:
integer count; integer addr [3:0]; initial
begin
Integer integer1, integer2,……….integer n [msb:lsb]
count=count+1;

## Slide 35: DATA TYPES
REGISTERS TYPES
(b) REAL
Real registers are used to specify the variable in decimal or scientific
notation and they are declared with the keyword real
Real numbers cannot have a range declaration and their default value is 0, its syntax is given as
Examples:
real pwd; initial begin
pwd=3e5; pwd=2.13;
end
Real real_reg1, real_reg2,……………….real_regn
35

## Slide 36: DATA TYPES
REGISTERS TYPES
(c) TIME
Time register is used to store and manupulate time values
They are used to store simulation time and it is declared with the keyword time
Syntax:
Examples:
time currtime; initial
begin
currtime=$time; end
Time time_id1, time_id2,………………..time_idn

## Slide 37: DATA TYPES
REGISTERS TYPES
(d) VECTORS
Net or reg data can be declared as vector, if bit width is not specified, the default
is scalar (1-bit)
Examples:
wire b; //scalar net variable wire[7:0] databus; //8-bit data bus
Represent buses
wire[3:0] busA;
reg [1:4] busB;
reg [1:0] busC;
Left number is MS bit
Vector assignment (by position!!)
busB[1] | = | busA[3];
busB[2] | = | busA[2];
busB[3] | = | busA[1];
busB[4] | = | busA[0];

## Slide 38: DATA TYPES
REGISTERS TYPES
types and array are accessed by:
(e)ARRAY
Array are used to declare multi-dimensional variable
Array types are used for reg, integer, data
<array_name>[<subscript>]
Examples:
integer matrix[4:0][0:255]; //two dimensional array of integer
reg[7:0] array1[3:0]; //declare an array of 8-bit vector reg
Syntax
integer count[1:5];//5 integers reg var[-15:16];//32 1-bit regs
reg [7:0] mem[0:1023];//1024 8-bit regs
Accessing array elements
Entire element: mem[10] = 8’b10101010;
Element subfield (needs temp storage):
reg [7:0] temp; temp = mem[10]; var[6] = temp[2];
Limitation: Cannot access array subfield or entire array at once
var[2:9] = ???;//WRONG!! var = ???;//WRONG!!
Arrays don’t work for the Real data type
real r[1:10];//WRONG !!

## Slide 39: DATA TYPES
REGISTERS TYPES
(f) MEMORIES
A memory is an array of registers it is simply a one-dimensional array of registers
Each element of array is known as element or word and it is addressed by single array index
A memory component can be defined using reg variables
4 3 2 1 0
myMem[0] myMem[1] myMem[2]
myMem[3]
reg [7:0] myMem [3:0];
Bit 7 6 5
// It defines a memory with 4 locations and each
// location contains an 8-bit data

## Slide 40: DATA TYPES
REGISTERS TYPES
(g) PARAMETERS
It is a constant and it is used to specify delays and widths of a variables
Parameter can be assigned a value only once using declaration and its form is
parameter param1=const_expr1, param2=const_expr2,…….paramN=const_exprN;
Parameter can be changed at compilation time using def param statement
Example:
……
parameter bussize = 8;
Parameter bit=1, byte=8; reg [bussize-1 : 0] databus;
……

## Slide 41: DATA TYPES
RESTRICTION ON DATA TYPES
Data Flow and Structural Modeling
  Can use only wire data type
  Cannot use reg data type
Behavioral Modeling
  Can use only reg data type
(within initial and always constructs)
  Cannot use wire data type

## Slide 43: OPERATORS
ARITHMETIC OPERATORS
 +, -, *, /, %,**
If any operand is x the result is x
Negative registers:
-regs can be assigned negative but are treated as unsigned
reg [15:0] regA;
..
regA = -4’d12; // stored as 216-12 = 65524
regA/3 evaluates to 21861

## Slide 44: OPERATORS
LOGICAL OPERATORS
&&  logical AND
||  logical OR
!  logical NOT
Operands evaluated to ONE bit value: 0, 1 or x
Result is ONE bit value: 0, 1 or x
A = 1;
B = 0; C = x;
A && B  1 && 0  0
A || !B  1 || 1  1 C || B  x || 0  x

## Slide 45: OPERATORS
RELATIONAL OPERATORS
>  greater than
<  less than
>=  greater or equal than
<=  less or equal than
Result is one bit value: 0, 1 or x
1 > 0
’b1x1 <= 0
10 < z
 1
 x
 x

## Slide 46: OPERATORS
EQUALITY OPERATORS
 ==  logical equality
!=  logical inequality
 === case equality
!==  case inequality
Return 0, 1 or x
Return 0 or 1

## Slide 47: OPERATORS
BITWISE OPERATORS
&  bitwise AND
|  bitwise OR
~  bitwise NOT
^  bitwise XOR
~^ or ^~  bitwise XNOR
c = ~a;
Operation on bit by bit basis
c = a & b;
c = a ^ b;

## Slide 48: OPERATORS
&
|
^
~&
~|
~^ or ^~
REDUCTION OPERATORS
 AND
 OR
 XOR
 NAND
 NOR
 XNOR
One multi-bit operand  One single-bit result
a = 4’b1001;
c = |a; // c = 1|0|0|1 = 1

## Slide 49: OPERATORS
SHIFT OPERATORS
>>  shift right
<<  shift left
Result is same size as first operand, always zero filled
// d = 0010
// c = 0100
a = 4’b1010; d = a >> 2;
c = a << 1;
>>>  arithmetic shift right
<<<  arithmeticshift left
Vacant position filled by either LSB (>>>) or MSB (<<<) value
a = 4’b0101;
d = a >>>1; c = a <<<1;
// d = 1010
// c = 1010

## Slide 50: OPERATORS
CONCATENATION OPERATORS
{op1, op2, ..}  concatenates op1, op2, .. to single number
Operands must be sized !!
reg a;
reg [2:0] b, c;
..
a = 1’b 1;
b = 3’b 010; c = 3’b 101;
catx = {a, b, c};
caty = {b, 2’b11, a};
catz = {b, 1};
// catx = 1_010_101
// caty = 010_11_1
// WRONG !!
Replication ..
catr = {4{a}, b, 2{c}};
// catr = 1111_010_101101

## Slide 51: OPERATORS
CONDITIONAL OPERATORS
cond_expr ? true_expr : false_expr
Like a 2-to-1 mux ..
Y = (sel)? A : B;
A
Y
B 0
1
sel
For 4-to-1 mux ..

## Slide 52: OPERATORS
OPERATORS PRECEDENCE
Use parentheses to
enforce your priority

## Slide 53: VERILOG MODELING
BEHAVIORAL
STRUCTURAL
DATA FLOW
SWITCH
Our focus

## Slide 54
63

## Slide 55: STRUCTURAL MODELING
At gate level, the circuit is described in terms of gates (e.g., and, nand)
Hardware design at this level is intuitive for a user with a basic knowledge of digital logic design
Because it is possible to see a one-to-one correspondence between the logic circuit diagram and the Verilog description
Actually, the lowest level of abstraction is switch- (transistor-) level modeling
However, with designs getting very complex, very few hardware designers work at switch level. So most of the digital design is now done at gate level or higher levels of abstraction.

## Slide 56: STRUCTURAL MODELING
GATE PRIMITIVES
All logic circuits can be designed by using basic gates. Verilog supports basic logic gates as predefined primitives. There are three classes of basic gates.
Multiple-input gates: and, or, nand, nor, xor, xnor
Multiple-output gates: buffer, not
Tristate gates: bufif0, bufif1, notif0, notif1
These primitives are instantiated like modules except that they are predefined in Verilog and do not need a module definition.
Logic gates can be used in design using gate instantiation. A simple format of a gate instantiation is,
Gate_type [instance_name] (term1, term2,……………..termn);

## Slide 57: STRUCTURAL MODELING
AND GATE
// Module Name: Andgate
module Andgate(i1, i2, out); input i1;
input i2; output out; and (out,i1,i2);
endmodule
OR GATE
// Module Name: Orgate
module Orgate(i1, i2, out);
input i1;
input i2; output out; or(out,i1,i2);
endmodule
Basic syntax for multiple-input gates is:
Multiple_input_Gate_type [instance_name] (output, input1, input2,……..inputn);

## Slide 58: STRUCTURAL MODELING
NAND GATE
// Module Name: Nandgate module Nandgate(i1, i2, out);
input i1; input i2; output out;
nand(out,i1,i2); endmodule
NOR GATE
// Module Name: Norgate module Norgate(i1, i2, out);
input i1;
input i2;
output out; nor(out,i1,i2);
endmodule

## Slide 59: STRUCTURAL MODELING
XOR GATE
// Module Name: Xorgate
module Xorgate(i1, i2, out);
input i1; input i2; output out; xor(out,i1,i2);
endmodule
XNOR GATE
// Module Name: Xnorgate module Xnorgate(i1, i2, out);
input i1;
input i2; output out; xnor(out,i1,i2);
endmodule
BECE102L – DIGITAL SYSTEM DESIGN
58

## Slide 60: STRUCTURAL MODELING
// Module Name: Notgate module Notgate(in, out);
input in; output out; not(out,in);
BUFFER GATE
// Module Name: Buffer
module Buffer(in, out);
input in; output out; buf(out,in);
endmodule
NOT GATE
Basic syntax for multiple-output gates is:
Multiple_output_Gate_type [instance_name] (output1, output2,……..outputn, input);
endmodule
BECE102L – DIGITAL SYSTEM DESIGN

## Slide 61: STRUCTURAL MODELING
// Module Name: Bufif1 module Bufif1(in, out, con);
input in,con; output out; bufif1(out,in,con);
endmodule
BUFIF1 GATE
BUFIF0 GATE
Basic syntax for tristate-gates is:
Tristate_type [instance_name] (output,input,control);
in
out
con
Out=in if con=1
Else out=Z
// Module Name: Bufif0 module Bufif0(in, out, con);
input in,con; output out; bufif0(out,in,con);
in
out
con
Out=in if con=0 Else out=Z
endmodule
BECE102L – DIGITAL SYSTEM DESIGN

## Slide 62: STRUCTURAL MODELING
// Module Name: notif1
module notif1(in, out, con);
input in,con; output out; notif1(out,in,con);
endmodule
NOTIF1 GATE
NOTIF0 GATE
// Module Name: notif0 module notif0(in, out, con);
input in,con;
output out; notif0(out,in,con);
endmodule
in
out
con
Out=in if con=1 Else out=Z
in
out
con
Out=in if con=0
Else out=Z

## Slide 63
STRUCTURAL MODELING
EXAMPLE – 2:1 MUX

## Slide 64
STRUCTURAL MODELING
MODULE

## Slide 65
STRUCTURAL MODELING
MODULE NAME

## Slide 66
STRUCTURAL MODELING
PORT LIST

## Slide 67
STRUCTURAL MODELING
INPUT/OUTPUT DECLARATION

## Slide 68
STRUCTURAL MODELING
DATA TYPE DECLARATION

## Slide 69
STRUCTURAL MODELING
GATE INSTATIATION

## Slide 70
STRUCTURAL MODELING
GATE INSTATIATION

## Slide 71: STRUCTURAL MODELING
// Module Name: HalfAdder module HalfAdder(sum, c_out, i1, i2);
output sum; output c_out; input i1; input i2; xor(sum,i1,i2);
and(c_out,i1,i2);
endmodule
HALF ADDER

## Slide 72: STRUCTURAL MODELING
FULL ADDER USING MODULE INSTATIATION
// Module Name: FullAdder
module FullAdder(sum, c_out, i1, i2,c_in); output sum;
output c_out; input i1; input i2; input c_in; wire s1,c1,c2;
HalfAdder HA1(s1, c1, i1, i2); HalfAdder HA2(sum, c2 ,s1,c_in); or(c_out,c1,c2);
endmodule
71

## Slide 73: STRUCTURAL MODELING
4-BIT PARALLEL ADDER USING MODULE INSTATIATION
module adder_4bit (S, COUT,A,B); output [3:0]S ;
output COUT ; input [3:0] A ;
input [3:0] B ;
wire [2:0]C;
FullAdder FA0(S[0],C[0],A[0],B[0],1'b0);
FullAdder FA1(S[1],C[1],A[1],B[1],C[0]);
FullAdder FA2(S[2],C[2],A[2],B[2],C[1]);
FullAdder FA3(S[3],COUT,A[3],B[3],C[2]);
endmodule
71

## Slide 74: STRUCTURAL MODELING
// Module Name: Mux4to1
module Mux4to1(i0, i1, i2, i3, s0, s1, out); input i0;
input i1; input i2; input i3; input s0; input s1; output out;
wire s1n,s0n; wire y0,y1,y2,y3; not (s1n,s1);
not (s0n,s0);
and (y0,i0,s1n,s0n);
and (y1,i1,s1n,s0);
and (y2,i2,s1,s0n);
and (y3,i3,s1,s0);
or (out,y0,y1,y2,y3); endmodule
4:1 MUX

## Slide 75: STRUCTURAL MODELING
1:4 DEMUX
// Module Name: Dux1to4
module Dux1to4(in, s0, s1, out0, out1, out2, out3);
input in; input s0; input s1; output out0; output out1; output out2; output out3; wire s0n,s1n; not(s0n,s0);
not(s1n,s1);
and (out0,in,s1n,s0n); and (out1,in,s1n,s0); and (out2,in,s1,s0n); and (out3,in,s1,s0);
endmodule

## Slide 76: STRUCTURAL MODELING
2:4 DECODER
FULL ADDER

## Slide 77: STRUCTURAL MODELING
EXERCISE
Binary Subtractor
Parallel Adder
Binary Multiplier
Magnitude Comparator-4 bit
Decoders
Encoders
Mux
Demux
Parity generator and checker.

## Slide 79: BEHAVIORAL MODELING

## Slide 80: BEHAVIORAL MODELING
Behavioral model enables you to describe the system at a higher level of abstraction
All we need to do is to describe the behavior of our design
  Action  How the model of our circuit should behave?
  Timing control  At what time do what thing & At what condition do what thing
Verilog supports the following construct to model circuit behavior
  Procedural block
  Procedural assignment
  Timing controls
  Block statement
  Conditional statement

## Slide 81: BEHAVIORAL MODELING
PROCEDURAL BLOCK
In Verilog procedural block are the basic of behavior modeling
  We can describe a one logic in one procedural block
  Procedural block types: (i) initial (ii) always
All initial & always statement execute concurrently starting at time t=0
A module may contain any number of initial & always statement
Structure of procedural block
type-of-block @ (sensitivity list)
begin : name-of-block; local variable declaration;
end
Type of block: initial or always
Symbol used to signifies event (only for always block)
Specify the event which starts the execution of the
procedural assignment statements;block (only for always block)
A block can assign a name for the block
Variables which are local to the block are defined here
This form the body of the block
All action within blocks are enclosed by begin- end construct

## Slide 82: BEHAVIORAL MODELING
PROCEDURAL BLOCK - INITIAL STATEMENT
Initial statement causes procedural statement to executes only once and it begin
its execution at start of simulation time 0.
Sequential block (begin-end) is the most commonly used procedural statement, that is it wait for a certain time until an event occurs
Syntax:
Example:
initial [timing_controls] procedural statements
initial #2 a=0
Example: //initial statement with sequential block reg a,b;
initial begin a=1`b0; b=1`b1; #5 a=1`b1; end;

## Slide 83: BEHAVIORAL MODELING
PROCEDURAL BLOCK - ALWAYS STATEMENT
For circuit synthesis we use the always block and such a block must contain all sequential constructs
Note that the statements in an always block between begin/end are executed sequentially just as they are written
Variables assigned a value inside an always block must be of type
reg or integer
The if, case, for loop, and while loop must appear inside an always block
A module can have multiple blocks, but blocks cannot be nested
For modules that have multiple always blocks all of the always blocks are executed in parallel

## Slide 84: BEHAVIORAL MODELING
in a digital circuit.
PROCEDURAL BLOCK - ALWAYS STATEMENT
Always blocks are repeated executed until simulation is stopped. Similar to initial block it begin its execution at start of simulation time 0.
This statement is used to model a block of activity that is repeated continuously
Syntax:
always [timing_control] procedural statement (or)
always @(sensitivity_list)
begin
/*sequential statements consisting of assignment,
if, case, while, and for loops */ end
Example:
module clock_gen;
reg clock, temp;
//Initialize clock at time zero
Initial clock = 1‘b0;
//Toggle clock every half-cycle always #10 clock = -clock;
always @ (posedge clock) begin
temp=temp+1; end

## Slide 85: BEHAVIORAL MODELING
PROCEDURAL STATEMENT
The assignment statement within an initial statement or always statement is called procedural statement
It is used to assign to only a register data type
Procedural statement executes sequentially respect to other statements that appear around it
Sequential block always start execution when an event occurs.
Two types of procedural assignments are: (i) blocking assignment
(ii) non-blocking assignment
Example: always @ (clk)
begin
reg count=z; count=count+1; z=count;
end

## Slide 86: BEHAVIORAL MODELING
procedural assignment
Blocking procedural assignment is executed before any of the statement that follow it are executed
The sum assignment occurs first, sum is computed, then second statement is executes C1 is assigned and then third executed and C2 is assigned and so on
Example:
// Full adder using blocking procedural statement
module FA(sum,cout,A,B,C)
input A,B,C; output sum, cout;
always @ ( A or B or C) begin
reg C1,C2,C3;
sum=A&C; C1=A&B; C2=B&C; C3=A&C;
Cout= C1|C2|C3; end
endmodule
BLOCKING PROCEDURAL ASSIGNMENT
A procedural statement in which the assignment operator is an “=“ in a blocking
Example: reg B=55;

## Slide 87: BEHAVIORAL MODELING
In non-blocking assignment the assignment symbol “<=“ is used
‘a’ is assigned the stored value of ‘b’ this activity is carried out concurrently
At the negative edge clock ‘c’ is assigned a value of b&(~c)
Two nanoseconds later positive edge clock assign ‘c’ value to ‘b’
Example:
always @ ( posedge clk) begin
a<=b;
@ (negedge clk) c<=b&(~c);
#2 b<=c;
endmodule
NON-BLOCKING PROCEDURAL ASSIGNMENT
The main characteristics of non-blocking assignment statement is execution is performed concurrently
Example: c<=a&b;

## Slide 88: BEHAVIORAL MODELING
BLOCKING vs NONBLOCKING
Blocking
<variable> = <statement>
Similar to C code
The next assignment waits until the present one is finished
Used for combinational logic
Non-blocking
<variable> <= <statement>
The inputs are stored once the procedure is triggered
Statements are executed in parallel
Used for flip-flops, latches and
registers
Do not mix both assignments in one procedure

## Slide 89: BEHAVIORAL MODELING
BLOCKING STATEMENT - SEQUENTIAL BLOCK
Block statements are used to group multiple statements to act together as one. There are two types of blocks: sequential blocks and parallel blocks
The keywords begin and end are used to group statements into sequential blocks.
Sequential blocks have the following characteristics:
  The statements in a sequential block are processed in the order they are specified
  A statement is executed only after its preceding statement completes execution
  If delay or event control is specified, it is relative to the simulation time when the previous statement in the
block completed execution
//Illustration 1: Sequential block without delay reg X, Y;
reg [1:0] z, w; initial
Begin
x = l'bO;
y = l‘b1;
z = {x, y};
w = {y, x}; End
//Illustration 2: Sequential blocks with delay reg x, y;
reg [1:0] z , w;
initial begin
x = l'bo; //completes at simulation time 0
#5 y = l'bl; //completes at simulation time 5 #10 z = {x, y}; //completes at simulation time 15 #20 w = {y, x); //completes at simulation time 35 end

## Slide 90: BEHAVIORAL MODELING
important.
The result of simulation remains the same except that all statements start in parallel at time 0. Hence, the block finishes at time 20 instead of time 35.
BLOCKING STATEMENT - PARALLEL BLOCK
Parallel blocks, specified by keywords fork and join, provide interesting simulation features
Parallel blocks have the following characteristics:
  Statements in a parallel block are executed concurrently
  Ordering of statements is controlled by the delay or event control assigned to each statement
  If delay or event control is specified, it is relative to the time the block was entered
All statements in a parallel block start at the time when the block was entered. Thus, the order in which the statements are written in the block is not
//Example : Parallel blocks with delay reg x, y;
reg [ 1 : 0 ] z, w; initial
fork
x = l'bO; //completes at simulation time 0 #5 y = l'b1; //completes at simulation time 5 #10 z {x, y}; //completes at simulation time 10 #20 w = {y, x}; //completes at simulation time join

## Slide 91: BEHAVIORAL MODELING
is executed
If condition_ 1 evaluates 0.x,z, then procedural_statement2 is not executed and an else branch, if it exist, is executed
CONDITIONAL STATEMENT - IF
Conditional statements are used for making decisions based upon certain
conditions
These conditions are used to decide whether or not a statement should execute
If the condition evaluates to a non zero known value, then procedural_statement1
Example:
module mux(out,a,b,sel); input a,b,sel; output out;
reg out; always @ (a,b) begin
if (sel==1’b0)
out=a; else out=b; end
endmodule
Syntax:
if (condition_1) procedural staement_1 else if (condition_2) procedural staement_2 else (condition_3) procedural staement_3

## Slide 92: BEHAVIORAL MODELING
BECE102L – DIGITAL SYSTEM DESIGN
90
UNIT-III : LECTURE30
The default_statement is optional.
CONDITIONAL STATEMENT - CASE
The keywords case, endcase, and default are used in the case statement
The expression is compared to the alternatives in the order they are written
For the first alternative that matches, the corresponding statement or block is executed. If none of the alternatives match, the default_statement is executed.
syntax:
case(case_expression)
case_item_expression {case_item_expression} procedural statement
………
……… default:procedural_statement endcase
module mux4_to_1 (out, iO, i1, i2, i3, sl, sO);
input iO, i1, i2, i3;
input s1. sO; //Port declarations from the I/O diagram
output out; reg out;
always @(sl or sO or iO or i1 or i2 or i3)
case ({sl, sO}) //Switch based on concatenation signals 2'dO out iO;
2'd1 out i1; 2'd2 out i2; 2'd3 out i3;
default: $display("Invalid control signals"); endcase
endmodule

## Slide 93: BEHAVIORAL MODELING
CONDITIONAL STATEMENT - CASE
Case treats each value 0, 1, x, and z literally
  4ʼb01xz only matches 4ʼb01xz
  Example: 4ʼb0110 does not match 4ʼb01xx in a case
Casez treats 0, 1, and x literally
  Casez treats z as a donʼt care
  Example: 4ʼb0110 matches 4ʼb01zz, but not 4ʼb01xz
Casex treats 0 and 1 literally
  Casex treats both x and z as donʼt cares
  Example: 4ʼb0110 matches 4ʼb01xx and also 4ʼb01xz
91

## Slide 94: BEHAVIORAL MODELING
CONDITIONAL STATEMENT - FORLOOP
When a circuit exhibits regularity, a for loop can be used inside an always statement to simplify the design description (for loop is a procedural statement used only inside an always block)
C style syntax: for (k = 0; k < 4; k = k+1)
  Loop index must be type integer (not reg!)
  Can`t use the convenience of k++
  Use begin …end for multiple statements in the loop
Each iteration of the loop specifies a different piece of the circuit
  Has nothing to do with changes over “time”
92

## Slide 95: BEHAVIORAL MODELING
CONDITIONAL STATEMENT - WHILE LOOP
All looping statements can appear only inside an initial or always block. Loops
may contain delay expressions
The while loop executes until the while-expression becomes false. If the loop is entered when the while-expression is false, the loop is not executed at all
If multiple statements are to be executed in the loop, they must be grouped
typically using keywords begin and end.
syntax:
While(condition)
Procedural_statements
//Increment count from 0 to 127. Exit at count 128.
integer count; initial
begin count = 0;
while (count < 128) begin
$display("Count = %d", count); //Display the count count = count + 1;
end
93

## Slide 96: BEHAVIORAL MODELING
starts and not during the loop execution.
CONDITIONAL STATEMENT - REPEAT LOOP
The keyword repeat is used for this loop. The repeat construct executes the loop a fixed number of times.
A repeat construct cannot be used to loop on a general logical expression. A while loop is used for that purpose.
A repeat construct must contain a number, which can be a constant, or a variable value.
However, if the number is a variable or signal value, it is evaluated only when the loop
syntax:
repeat [loop count] procedural_statement
//EXAMPLE : increment and display count from a to 127 integer count;
initial begin count = 0; repeat(128) begin
$display("Count = %d", count); count = count + 1;
end end
94

## Slide 97: BEHAVIORAL MODELING
CONDITIONAL STATEMENT - FOREVER LOOP
The keyword forever is used to express this loop. A forever loop can be exited by
use of the disable statement.
The loop does not contain any expression and executes forever until the $finish task is encountered.
The loop is equivalent to a while loop with an expression that always true, e.g.,
while (1).
A forever loop is typically used in conjunction with timing control constructs.
syntax:
forever procedural_statement
//Example : Clock generation
//Use forever loop instead of always block reg clock;
initial
begin
clock = 1'b0;
forever #10 clock=-clock; //Clock with period of 20 units end
95

## Slide 98
BEHAVIORAL MODELING
FULL ADDER
96

## Slide 99
BEHAVIORAL MODELING
4x1 MUX
97

## Slide 100
BEHAVIORAL MODELING
2 to 4 DECODER
98

## Slide 101
BEHAVIORAL MODELING
2 to 4 DECODER
99

## Slide 102
BEHAVIORAL MODELING
4 to 2 ENCODER
100

## Slide 103
BEHAVIORAL MODELING
4 to 2 PRIORITY ENCODER
101

## Slide 104
BEHAVIORAL MODELING
4 to 2 PRIORITY ENCODER
102

## Slide 105
103

## Slide 106: DATAFLOW MODELING
Data flow level description of a digital circuit is at higher level, it makes the circuit description more compact as compared to design through gate primitives
Design implement using data flow modeling uses a continuous assignment statement and Verilog provides different operators to perform a function
The assignment statement start with the keyword assign and results are
assigned to nets
Continuous assignment – most basic statement used to drive value onto net
Syntax: assign LHS_target=RHS_expression
104
Example:
wire c,a,b; //net declaration
assign c=a&b; //continuous assignment

## Slide 107: DATAFLOW MODELING
Implicit continuous assignment – it is the shortcut method of assigning the
expression on the net
Implicit net declaration – if a signal name of the left hand side of the continuous assignment statement is not declared the verilog simulator assign an implicit net declaration for the net
Example:
//regular continuous assignment wire c,a,b;
assign c=a&b;
//implicit continuous assignment wire c=a&b;
Example: //continuous assignment wire a,b;
assign c=a&b; // here c is not declared as a wire
/* but simulator automatically delare it as wire if we use implicit net delaration statement */
105

## Slide 108: DATAFLOW MODELING
Regular assignment delay – the assignment takes effect with the time delay of 2 time steps. If the values of ‘a’ and ‘b’ changes then ‘c’ wait for two time steps to compute the result.
Implicit continuous assignment delay – it is a shortcut method of assigning the delay
and the expression on the net
Net declaration delay – a delay can be specified on a net when it is declared without
putting a continuous assignment on the net
Example:
wire c,a,b;
assign #2 c=a&b;
Example: wire #5 c=a&b;
Example:
106
wire #5 c; assign c=a&b;

## Slide 109: DATAFLOW MODELING
EXPRESSIONS
An expression is formed using operands & operators
Expression can be used whenever a value is expected
Example: a & b, x1[7:0] + x2[7:0]
OPERANDS
Operands are the data types used in the expression
An operands can be constant, net, parameter, register, memory, bit select
Example: c = a + b // a, b, c are real operands
OPERATORS
Operators act on operands to produce desired result
Various types: arithmetic, logical, relational, equality, bitwise, shift, etc.,
Example: c = a % b // % is operator to perform modules operation on a,b
107

## Slide 110: DATAFLOW MODELING
FULL ADDER
module fa_da(a,b,cin,sum,cout); input a,b,cin;
output sum,cout; assign sum=a^b^cin;
assign cout=(a&cin)|(b&cin)|(a&b); endmodule
108
HALF ADDER
module halfadder(s,c,a,b); input a,b;
output s,c; assign s=a^b; assign c=a&b; endmodule

## Slide 111: DATAFLOW MODELING
module mux(y,s,i); input [2:0]s;
input[7:0]i;
output y;
assign y= (~s[2] & ~s[1] & ~s[0] & i[1]) | (~s[2] &
~s[1] & s[0] & i[2]) | (~s[2] & s[1] & ~s[0] &
i[3]) | (~s[2] & s[1] & s[0] & i[4]) | (s[2] & ~s[1] &
~s[0] & i[5]) | (~s[2] & s[1] & ~s[0] & i[6]) | (s[2] &
s[1] & ~s[0] & i[7]) | (s[2] & s[1] & s[0] & i[8]);
endmodule
109
8:1 MUX

## Slide 112: DATAFLOW MODELING
BINARY TO GRAY CODE CONVERTER
module binary_to_gray(g,b); input [3:0]b;
output[3:0]g;
assign g[3]= b[3];
assign g[2]= b[2]^b[3];
assign g[1]= b[1]^b[2];
assign g[0]= b[0]^b[1]; endmodule
110

## Slide 113: DATAFLOW MODELING
assign e2=d[4]^d[5]; assign e3=d[6]^d[7]; assign f0=e0^e1; assign f1=e2^e3; assign h0=f0^f1; assign odd=h0^d[8]; assign even=~odd; endmodule
9-BIT PARITY GENERATOR
module parity(even,odd,d); input [8:0]d;
output even, odd;
wire e0,e1,e2,e3,f0,f1,h0; assign e0=d[0]^d[1]; assign e1=d[2]^d[3];
d[8]
d[0] | e0 | 
d[1] |  | f0
d[2] |  | 
d[3] | e1 | h0
d[4] d[5] | e2 | 
d[6] d[7] | e3 | f1
111
even odd

## Slide 114: DATAFLOW MODELING
8:3 PRIORITY ENCODER
module PriorityEncoder_DataFlow(code,data); input[7:0]data;
output[2:0]code;
wire [7:0]w;
assign w[0]=(~data[0]);
assign w[1]=(~data[1]);
assign w[2]=(~data[2]);
assign w[3]=(~data[3]);
assign w[4]=(~data[4]);
assign w[5]=(~data[5]);
assign w[6]=(~data[6]);
assign w[7]=(~data[7]);
assign code[0]=(w[7]&w[6]&w[5]&w[4]&w[3]&w[2]&data[1])|
(w[7]&w[6]&w[5]&w[4]&data[3])|(w[7]&w[6]&data[5])|data[7];
assign code[1]=(w[7]&w[6]&w[5]&w[4]&w[3]&data[2])|
(w[7]&w[6]&w[5]&w[4]&data[3])|(w[7]&data[6])|data[7];
assign code[2]=(w[7]&w[6]&w[5]&data[4])|(w[7]&w[6]&data[5])|(w[7]&data[6])|data[7]; endmodule
112

## Slide 115
113

## Slide 116: TEST BENCH
INTRODUCTION
We need to apply appropriate stimulus to the design in order to test it. This can be done by writing another Verilog code called the ‘Test Bench’. This is written as a separate file, different from the design file(s).
Stimulus is nothing but the application of various permutations and combinations of inputs at various points of time and, looking for correct results produced by the design.
The design may comprise of just one module or several modules depending upon the complexity of the application. As mentioned earlier, the test bench applies appropriate test pattern to the inputs of the design under test and checks the outputs of the design so as to verify its functionality.
114

## Slide 117: TEST BENCH
STRUCTURE
module test_module_name;
//declare local reg and wire identifiers.
//instantiate the design module under test
//generate stimulus (inputs to design module) using initial and always.
// display output response.(display on screen or print)
endmodule
Examples:
$display("%d %b %b",A,B,C);
$monitor($time„"%b %b %h" , s1,s2,outvalue);
115

## Slide 118
TEST BENCH
INTRODUCTION
116

## Slide 119
TEST BENCH
INTRODUCTION
117

## Slide 120: TEST BENCH
118

## Slide 121: TEST BENCH – AND GATE
119

## Slide 122: TEST BENCH – HALF ADDER
120

## Slide 123: TEST BENCH – FULL ADDER
121

## Slide 124: TEST BENCH – FULL ADDER
122

## Slide 125: TEST BENCH – 4:1 MUX
123

## Slide 126: TEST BENCH – 4:1 MUX
124

## Slide 127: TEST BENCH – D-FLIP FLOP
D FLIPFLOP
module dflipflopmod(q, d, clk); output q;
input d;
input clk; reg q;
always @(posedge clk) q=d;
endmodule
124
TEST BENCH:
module dflipflopt_b;
reg d; reg clk; wire q;
dflipflopmod uut (.q(q),.d(d), .clk(clk) );
initial begin
// Initialize Inputs d = 0;
clk = 0; end
always #3 clk=~clk;
always #5 d=~d; endmodule

## Slide 128: DEBUGGING AND ERROR CHECKING
The following Verilog code is supposed to describe a circuit that has an 8- bit data input, an 8-bit data output, plus two additional single-bit outputs. The over_flow output is strictly combinatorial. You may assume that the operations to produce data_out, carry_out and over_flow are correct (i.e. the functional specification for these values is correct). However, syntax errors for these statements do exist.
Examine the code below and identify any errors that would prevent this code from compiling and synthesizing properly. These errors may include syntax errors, logical design errors or needed lines that are missing from the code. Indicate the modifications you would make to the code to make it work. Include comments beside these modifications or the portion of the code that is incorrect. There are 20 errors in the code below.
125

## Slide 129: DEBUGGING AND ERROR CHECKING
module bad_module is (clk,
reset,
[7:0] data_in,
data_out; carry out, over_flow )
input clk; input reset; input carry_in; input data_in;
output data_out; output carry_out; output over_flow; reg [7:0] data_out;
reg carry_out, overflow;
126

## Slide 130: DEBUGGING AND ERROR CHECKING
always @ (posedge clk | posedge reset) ; if reset
then data_out = 0;
carry_out = 0;
Else
data_out = (data_in * 2) + carry_in; carry out = ~& data_in[7,6];
over_flow = data_out(7);
end module
127

## Slide 131: DEBUGGING AND ERROR CHECKING
(1) Removed “is” after module
128
Removed [7:0]
Added carry_in
Changed “;” to “,”
Changed “carry out” to “carry_out”
Semicolon at the end of module definition
Added [7:0]
Added [7:0]
module bad_module (clk,
reset, data_in,
carry_in, data_out, carry_out, over_flow )
input clk; input reset; input carry_in;
input [7:0] data_in;
output [7:0] data_out;
output carry_out;
output over_flow; reg [7:0] data_out; reg carry_out;
;

## Slide 132: DEBUGGING AND ERROR CHECKING
always @ (posedge clk or posedge reset)
if (reset)
begin data_out = 0;
carry_out = 0; end
else begin
data_out = (data_in * 2) + carry_in; carry_out = ~& data_in[7:6];
end
assign over_flow = data_out[7]; endmodule
129
Changed “|” to “or”
No semicolon for always statement
Added Parentheses around “reset”
Removed “then”
Added “begin”
Added “end”
“else” keyword must be lower case
Added “begin”
Replace “,” with “:”
Added “end”
Changed “out7” to “out[7]”
Removed space between “end” & “module”